## Slide 1: Topic 4
Procedure Calling
(Modified by J. Nelson Amaral)

## Slide 3: Procedure calls
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }

## Slide 4: Procedure calls
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
caller
callee
caller
callee
return address
must remember return address
must return to correct return address
return address
return address

## Slide 5: Problem
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
write return address into $ra
In MIPS there is a single register,
$ra, to store the return address.
overwrite return
address into $ra
return to wrong address
return to correct
address

## Slide 6: Solution
We need to save the value of $ra somewhere.
Where?
Into a stack.

## Slide 7: What goes into the stack
The value of the register $ra
(if the function calls another function).
Any register that is modified by the function.
Any local variables that need memory storage.
The value of the register $fp.
Stack

## Slide 8: Where is the top of the Stack?
MIPS has a special register
called stack pointer ($sp)
$sp always contains the
address of the top of the stack.
Stack
0x4000 0FF0
0x4000 0FEC
0x4000 0FE8
0x4000 0FE4
0x4000 0FE0
0x4000 0FDC
0x4000 0FD8
0x4000 0FD4
0x4000 0FD0
$sp
0x4000 0FF0

## Slide 9: Saving Register into the Stack
$sp
Memory
↑ High Address
↓ Low Address
0x1000 4004
$ra
Problem: a subroutine will write on $a0
and call another subroutine.
Must save values of $a0, $fp and $ra into the stack.
0x1000 2000
$sp
How do we make room in the stack for these
three registers?
The stack grows towards lower memory addresses.
0x0000 0003
$a0
0x1000 200C
$fp

## Slide 10: Saving Register into the Stack
0x0000 0003
0x1000 4004
Problem: a subroutine will write on $a0
and call another subroutine.
Must save values of $a0 and $ra into the stack.
0x1000 2000
How do we make room in the stack for these
two registers?
The stack grows towards lower memory addresses.
$sp
Memory
↑ High Address
We need to decrement the value of $sp by 12.
0x1000 1FF4
How do we actually “save” $a0, $ra and $fp?
Write their values, using the sw instruction,
to the stack:
0x1000 200C
$ra
$sp
$a0
$fp
sw $a0, 4($sp)
↓ Low Address
0x1000 200C
0x0000 0003
0x1000 4004

## Slide 11: Solution
1: void foo()
2: {
3: int a, b;
4: scanf(“%d %d”,&a, &b);
5: …
6: r = bar(a, b);
7: t = 2*r;
8: …
9: r = bar(b, a);
10: c = c + 4*r;
11: …
12: }
1: int bar(int x, int y)
2: {
3: int i, p, t;
4: t = 1;
5: for(i=0, i<y ; i++){
6: t = baz(x);
7: p = p*t;
8: }
9: return p;
10: }
1: int baz(int d)
2: {
3: int z;
4: z = 100-d;
5: return z;
6: }
write return address into $ra
In MIPS there is a single register,
$ra, to store the return address.
safe to overwrite return
address into $ra
return to correct address
save $ra into stack
restore $ra from stack
return to correct
address

## Slide 12: Saving Register into the Stack
0x0000 01F7
$a0
0x1000 41F8
$ra
How do we “restore” the values of $a0, $fp, and $ra?
0x1000 2000
$sp
Do we need to do anything to the value of $sp?
Now the procedure has completed its execution and
it it time to return to the caller.
$sp
Memory
↑ High Address
↓ Low Address
Yes, we need to increment the value of $sp by 12.
0x1000 1FF4
Read their values, using the lw instruction,
from the stack.
0x0000 0003
0x1000 4004
0x0000 0003
0x1000 4004
0x0000 0003
0x1000 4004
0x1000 2004
$fp
0x1000 200C
0x1000 200C
0x1000 200C

## Slide 13: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
Section 2.8

## Slide 14: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
Section 2.8

## Slide 15: Optimization
It would be wasteful if every callee had to save/restore every register that it uses.
  The callee might be saving/restoring registers that are not in use by the caller at the call point.
Register context calling convention:
  Some registers are reserved for use by caller
  Others are reserved for callee

## Slide 16: Concept of Liveness
A register is live if it contains a value that may be used in the future.
A register is dead if it contains a value that will never be used in the future.

## Slide 17: Live and Dead --- Example
add $t0, $a0, $a1
add $t1, $a2, $a3
sub $s0, $t0, $t1
add $v0, $s0, $zero
sw $s0, 0($sp)
addi $sp, $sp, -4
lw $s0, 0($sp)
addi $sp, $sp, 4
jr $ra
foo:

## Slide 18: Calling Convention
foo{
…
bar();
….
}
bar(){
….
}
Save live caller-saved registers.
Save callee-saved registers that are
written by the callee.
Restore saved callee-saved registers.
Restore live caller-saved registers.

## Slide 19: Register Saving Convention
To avoid saving and restoring dead registers, MIPS
adopts the following software convention:
These names indicates which procedure (the caller or the callee)
is responsible for preserving the value stored in the register
at the procedure boundary.
Section 2.8
Registers $t0-$t9 are not preserved by the callee on a
procedure call.
Registers $s0-$s7 must be preserved on a procedure call.
Registers $t0-$t9 are the caller-saved registers
Registers $s0-s7 are callee-saved registers.

## Slide 20: Registers Used for Procedure Calls
$a0-$a3: four argument registers in which to pass parameters
$v0-$v1: two value registers in which to return values
$ra: one return address register to return to the point of origin
Section 2.8

## Slide 21: Register Usage Convention
Section A.6/B.6

## Slide 22: Register Usage Convention
Section A.6/B.6

## Slide 23: Register Usage Convention
Section A.6/B.6

## Slide 24: Register Usage Convention
Section A.6/B.6

## Slide 25: Register Usage Convention
Section A.6/B.6

## Slide 26: Register Usage Convention
Section A.6/B.6

## Slide 27: Register Usage Convention
Section A.6/B.6

## Slide 28: Register Usage Convention
Section A.6/B.6

## Slide 29: Register Usage Convention
Section A.6/B.6

## Slide 30: Register Usage Convention
Section A.6/B.6

## Slide 31: Register Usage Convention
Section A.6/B.6

## Slide 32: An illustration of the MIPS register calling convention

## Slide 33
caller
callee
$t0-$t7
$s0-$s7
I must save values
that I need later from
$t0-$t7
Callee will
preserve values in
$s0-$s7

## Slide 34
$t0-$t7
$s0-$s7
caller
callee
I can use $t0-$t7
without saving
Must save $s0-$s7
before using
these registers

## Slide 35: Why do we need a Frame Pointer?

## Slide 36
$ra
x
y
a[2]
a[1]
a[0]
$sp
0x4000 0FF0
void foo (…){
…
bar();
…
}
C code:
Stack
0x4000 0FF0
0x4000 0FEC
0x4000 0FE8
0x4000 0FE4
0x4000 0FE0
0x4000 0FDC
0x4000 0FD8
0x4000 0FD4
0x4000 0FD0
…
0x4000 0FF4
0x4000 0FF8
int bar (…){
int x, y;
…
x = x + y;
if(…){
int a[3];
y = x+y
…
}
x = x+y;
}
0x4000 0FE4
lw $t0, 4($sp) # $t0  x
lw $t1, 0($sp) # $t1  y
0x4000 0FD8
lw $t4, 16($sp) # $t4  x
lw $t5, 12($sp) # $t5  y
…
bar’s
frame
bar’s
frame

## Slide 37
0x4000 0FF8
$ra
x
y
a[2]
a[1]
a[0]
$sp
0x4000 0FF0
void foo (…){
…
bar();
…
}
C code:
Stack
0x4000 0FF0
0x4000 0FEC
0x4000 0FE8
0x4000 0FE4
0x4000 0FE0
0x4000 0FDC
0x4000 0FD8
0x4000 0FD4
0x4000 0FD0
…
0x4000 0FF4
0x4000 0FF8
0x4000 0FE4
lw $t0, -4($fp) # $t0  x
lw $t1, -8($fp) # $t1  y
0x4000 0FD8
lw $t4, -4($fp) # $t4  x
lw $t5, -8($fp) # $t5  y
…
bar’s
frame
bar’s
frame
$fp
0x4000 0FEC
int bar (…){
int x, y;
…
x = x + y;
if(…){
int a[3];
y = x+y
…
}
x = x+y;
}

## Slide 38: Frame Pointer
Save $fp
Some procedures may change $sp during its execution. Then:
Move $fp
to first position of frame
Always use $fp to access stack
Restore $fp

## Slide 39: Frame Pointer (Example)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
0x1000101C
callee’s
frame

## Slide 40: Frame Pointer (Example – at begin)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
0x1000101C
callee’s
frame
sw $fp, 0($sp)
move $fp, $sp
add $sp, $sp, -12
sw $s0, -4($fp)
∙∙∙
addi $sp, $sp, -4
0xFADEF100
0xABCDEF00
0x12345678

## Slide 41: Frame Pointer (Example - at end)
0x10001000
0x10001020
0x1000101C
0x10001018
0x10001014
0x10001010
0x1000100C
0x10001008
0x10001004
$FP
caller’s
frame
$SP
callee’s
frame
addi $sp, $sp, 16
lw $s0, -4(fp)
∙∙∙
lw $fp, 0($fp)
0x1000101C
0xFADEF100
0x1000101C
0xFADEF100
0xABCDEF00
0x12345678
0xABCDEF00
0x12345678

## Slide 42: Procedure Call Instructions
jal ProcedureLabel
jr $ra
Section 2.8
Procedure call: jump and link
Procedure return: jump register
  Address of following instruction put in $ra
  Jumps to target address
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 43: Branch and Link
BGEZAL: Branch on greater than or equal to zero
and save return address in $ra.
Example:
bgezal $s0, offset
Operation:
PC ← PC + 4
if $s0 ≥ 0
$ra ← PC
PC ← PC + offset<<2
Binary representation:
0000 01ss sss1 0001 iiii iiii iiii iiii
link bit:
0: bgez
1: bgezal

## Slide 44: Branch and Link
BLTZAL: Branch on less than zero
and save return address in $ra.
Example:
bltzal $s0, offset
Operation:
PC ← PC + 4
if $s0 < 0
$ra ← PC
PC ← PC + offset<<2
Binary representation:
0000 01ss sss1 0000 iiii iiii iiii iiii
link bit:
0: bgez
1: bgezal

## Slide 45
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Execute callee
Place result in return register
add $v0, $zero, $t5
Return control to caller
jr $ra
Not using stack

## Slide 46
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, 0($sp)
sw $s0, 4($sp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, 0($sp)
lw $s0, 4($sp)
Return control to caller
jr $ra
Using stack
no $fp
Restore stack pointer
addi $sp, $sp, 8

## Slide 47
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Save $fp
addi $sp, $sp, -4
sw $fp, 0($sp)
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, -4($fp)
sw $s0, -8($fp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, -4($fp)
lw $s0, -8($fp)
lw $fp, 0($fp)
Restore stack pointer
addi $sp, $sp, 12
Return control to caller
jr $ra
Using stack
with $fp

## Slide 48
Place parameters in registers
add $a0, $zero, $t5
Transfer control to callee
jal my_cool_procedure
Save $fp
addi $sp, $sp, -4
sw $fp, 0($sp)
Callee Acquire storage
addi $sp, $sp, -8
Save callee-saved registers
sw $ra, -4($fp)
sw $s0, -8($fp)
Execute callee
Place result in return register
add $v0, $zero, $t5
Restore regs and $fp
lw $ra, -4($fp)
lw $s0, -8($fp)
lw $fp, 0($fp)
Restore stack pointer
addi $sp, $sp, 12
Return control to caller
jr $ra
Save caller-saved registers
addi $sp, $sp, -4
sw $t0, -8($fp)
Caller Acquire storage
Restore caller-saved registers
lw $t0, -8($fp)
addi $sp, 4
Restore stack pointer

## Slide 49: Leaf Procedure Example
Have to save $s0 on stack
C code:
int leaf_example (int g, h, i, j)
{
int f;
f = (g+h) - (i+j);
return f;
}
Section 2.8
Assumption:
g ↔ $a0
h ↔ $a1
i ↔ $a2
j ↔ $a3
f ↔ $s0
result ↔ $v0

## Slide 50: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j)
{
int f;
f = (g+h) - (i+j);
return f;
}
Section 2.8
add $t0, $a0, $a1 # $t0 ← g+h
add $t1, $a2, $a3 # $t1 ← i+j
sub $s0, $t0, $t1 # f ← (g+h) – (i+j)
add $v0, $s0, $zero # $v0 ← f
$s0 is a callee-saved register, therefore we need to save/restore it
$sp
↑ High Address
↓ Low Address
Memory
sw $s0, 0($sp) # save $s0
addi $sp, $sp, -4 # grow stack
lw $s0, 0($sp) # restore $s0
addi $sp, $sp, 4 # shrink stack
leaf_example:
0x0000 0004
0x0000 0004
jr $ra # return
Assumption:
g ↔ $a0
h ↔ $a1
i ↔ $a2
j ↔ $a3
f ↔ $s0
result ↔ $v0

## Slide 51: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to:
  Save on the stack:
    Arguments and temporaries needed after the call
  Restore values from the stack after the call
Section 2.8

## Slide 52: Calling Itself
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
Section 2.8

## Slide 53: The Factorial Function
save ($ra,$a0)
if (n < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
$v0 ← fact($a0);
restore ($ra,$a0);
tA ← n * $v0;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
$v0 ← fact($a0);
tA ← n * $v0;
restore $ra;
return(tA);
}
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
save $ra
if (n < 1){
restore $ra;
return(1);
}
else{
tA ← n * fact(n-1);
restore $ra;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
$a0 ← n-1;
tA ← n * fact($a0);
restore $ra;
return(tA);
}
save $ra
if (n < 1){
restore $ra;
$v0 ← 1;
return($v0);
}
else{
tA ← n * fact(n-1);
restore $ra;
return(tA);
}
save ($ra,$a0)
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
restore ($ra,$a0);
tA ← $a0 * $v0;
return(tA);
}

## Slide 54: The Factorial Function
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}
save ($ra,$a0)
if ($a0 < 1){
restore ($ra,$a0);
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
restore ($ra,$a0);
$v0 ← $a0 * $v0;
return($v0);
}
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
$sp ← $sp+8;
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}

## Slide 55: Recursive Procedure
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n < 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact: # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$sp ← $sp – 8;
M[$sp+4] ← $ra;
M[$sp] ← $a0;
if ($a0 < 1){
$sp ← $sp+8;
$v0 ← 1;
return($v0);
}
else{
$a0 ← $a0-1;
$v0 ← fact($a0);
$a0 ← M[$sp];
$ra ← M[$sp+4];
$sp ← $sp+8;
$v0 ← $a0 * $v0;
return($v0);
}
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 56
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
Section 2.8
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 57
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
$a0
Processor
0x1000 2000
$sp
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
$sp
Memory
↑ High Address
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 58
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 2000
$sp
$ra
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 59
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
$sp
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 60
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n <≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 61
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 62
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 63
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 64
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 4004
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 65
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
0x1000 4004
3
$sp
Memory
↑ High Address
↓ Low Address
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 66
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 67
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 68
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 69
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
$sp
Memory
↑ High Address
↓ Low Address

## Slide 70
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 71
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 72
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
↓ Low Address

## Slide 73
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
0
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 74
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 75
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0
$sp

## Slide 76
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 77
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
0
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 78
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
$sp
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 79
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FE8
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0
$sp

## Slide 80
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 81
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 82
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
1
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 83
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
2
$a0
Processor
0x1000 1FF0
$sp
0x1000 6FEC
$ra
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
↓ Low Address
0x1000 6FEC
0

## Slide 84
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
1
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 85
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 86
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
2
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 87
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
3
$a0
Processor
0x1000 1FF8
$sp
0x1000 6FEC
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
↓ Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 88
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
2
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 89
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
6
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 90
MIPS assembly:
fact:
subi $sp, $sp, 8 # Make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # if ($a0<1) then $t0←1 else $t0 ← 0
beq $t0, $zero, L1 # if n ≥ 1, go to L1
addi $v0, $zero, 1 # return 1
addi $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1: subi $a0, $a0, 1 # subtract 1 from argument
jal fact # call fact(n-1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n-1)
jr $ra # return to the caller
1
$t0
6
$v0
3
$a0
Processor
0x1000 2000
$sp
0x1000 4004
$ra
0x1000 4004
3
0x1000 6FEC
2
0x1000 6FEC
1
$sp
Memory
↑ High Address
0x1000 3FFB addi $a0,$zero,3
0x1000 4000 jal fact
0x1000 4004 ….
 Low Address
0x1000 6FEC
0
Pat.-Hen. pp. 136-138
and A-26/A-29
int fact ( int n )
{
if (n < 1)
return(1);
else
return(n * fact(n-1));
}

## Slide 91: Other Data Stored in the Stack
$sp
↑ High Address
↓ Low Address
$fp
Before procedure
call
$sp
↑ High Address
↓ Low Address
$fp
After procedure
call
$sp
↑ High Address
↓ Low Address
$fp
During procedure
call
Saved argument
registers
Saved return reg.
Saved
registers
Local arrays
and structures
Patt.-Hen. pp 139
P-H p. 119

## Slide 92: Instructions to maniputate characters (Bytes)
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword
Section 2.9

## Slide 93: How do I know by how much to multiply the index of an array?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Look at the size of each element of the array!
int X[100];
address(X[i]) = X + 4×i;
char S[100];
address(S[j]) = S + j;
base of X
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of S
address(F[k]) = F + 8×k;
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of F
double F[100];

## Slide 94: You can create an array of anything.
C code:
…
struct city {
int DistanceFromCoast;
int Population;
char Subway;
char RingRoad;
};
struct city T[150];
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
base of T
address(T[i]) = T + 10×k;

## Slide 95: String Copy Example
C code (naïve):
  Null-terminated string
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
Section 2.9
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }

## Slide 96
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if(y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
i ← 0; L1: $t2 ← y[i];
x[i] ← $t2;
if(y[i] == 0) goto L2;
i ← i+1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t2 ← y[$s0];
x[$s0] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Section 2.9

## Slide 97
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
Section 2.9
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
x[$s0] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: return;
Intermediate Code:
strcpy:
⟨save registers⟩
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: ⟨restore registers⟩
return;
Intermediate Code:
strcpy:
$sp ← $sp - 4
M[$sp] ← $s0
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: $s0 ← M[$sp]
$sp ← $sp + 4;
return;

## Slide 98
Intermediate Code:
strcpy:
$sp ← $sp - 4
M[$sp] ← $s0
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: $s0 ← M[$sp]
$sp ← $sp + 4;
return;
MIPS assembly:
strcpy:
addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $0, $0 # i ← 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 ← y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] ← y[i] beq $t2, $0, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i ← i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return
P-H p. 125
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1

## Slide 99
Intermediate Code:
strcpy:
$sp ← $sp - 4
M[$sp] ← $s0
$s0 ← 0; L1: $t1 ← $s0 + $a1;
$t2 ← M[$t1];
$t3 ← $s0 + $a0;
M[$t3] ← $t2;
if($t2 == 0) goto L2;
$s0 ← $s0 + 1;
goto L1;
L2: $s0 ← M[$sp]
$sp ← $sp + 4;
return;
P-H p. 125
C code:
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Assumption:
i ↔ $s0
x ↔ $a0
y ↔ $a1
MIPS assembly:
strcpy:
addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $0, $0 # i ← 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 ← y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] ← y[i] beq $t2, $0, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i ← i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return