## Slide 1: Topic A
Floating Point Representation
(modified by J. Nelson Amaral)

## Slide 2: Floating Point
Representation for non-integer numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
P-H. p. 242

## Slide 3: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
P-H. p. 241

## Slide 4: Floating Point Representation
Most standard floating point representation use:
1 bit for the sign (positive or negative)
8 bits for the range (exponent field)
23 bits for the precision (fraction field)
From: Patt and Patel, pp. 33
P-H. p. 245
S
1
fraction
23
biasedexponent
8
Most-Significant Bit (MSB)
Least-Significant Bit (MSB)
MSB
LSB

## Slide 5: Floating Point Representation (example)
Thus the exponent is given by:
1 10000001 10101000000000000000000
From: Patt and Patel, pp. 34
P-H. p. 245
S
biasedexponent
fraction
23
8
1

## Slide 6: Floating Point Representation (example)
0011 1101 1000 0000 0000 0000 0000 0000
What is the decimal value of the following floating point number?
biasedexponent
biasedexponent = 27 – 23 + 3 = 128 - 8 + 3 = 123
From: Patt and Patel, pp. 34
P-H. p. 245
S
biasedexponent
fraction
23
8
1

## Slide 7: Answering Dylan Ashley's Question (Fall 2014)
Why the IEEE standard use the bias format for the exponent
instead of a two-complement representation? Why?

## Slide 9: How to find the answer?

## Slide 11
1. Download the .pdf
2. Use search into the .pdf for what you want to find.
Example: "bias"

## Slide 13: Example
Problem: Compare 2.5 and 0.25. Which is larger?
2.5 = 21 + 2-1 = 10.1 × 20 = 1.01 × 21
0.25 = 2-2 = 0.01 × 20 = 1.0 × 2-2

## Slide 14: Example
Problem: Compare 2.5 and 0.25. Which is larger?
Representation with exponent in two complement:
Representation with exponent in bias representation:
2.5 = 1.01 × 21
0.25 = 1.0 × 2-2
2.5 = 0 10000000 01000000000000000000000
0.25 = 0 11111110 00000000000000000000000
-2 = 11111110
2.5 = 0 00000001 01000000000000000000000
0.25 = 0 01111101 00000000000000000000000

## Slide 15: Example
Problem: Compare 2.5 and 0.25. Which is larger?
Representation with exponent in two complement:
Representation with exponent in bias representation:
2.5 = 1.01 × 21
0.25 = 1.0 × 2-2
2.5 = 0 10000000 01000000000000000000000
0.25 = 0 11111110 00000000000000000000000
2.5 = 0 00000001 01000000000000000000000
0.25 = 0 01111101 00000000000000000000000
Using integer comparison:
2.5 < 0.25
Using integer comparison:
0.25 < 2.5