## Slide 1: Topic A
Floating Point Representation
(modified by J. Nelson Amaral)

## Slide 2: Floating Point
Representation for non-integer numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
P-H. Section 3.5

## Slide 3: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
P-H. Section 3.5

## Slide 4: Floating Point Representation
Most standard floating point representation use:
1 bit for the sign (positive or negative)
8 bits for the range (exponent field)
23 bits for the precision (fraction field)
From: Patt and Patel, pp. 33
S
1
fraction
23
biasedexponent
8
Most-Significant Bit (MSB)
Least-Significant Bit (MSB)
MSB
LSB
P-H. Section 3.5

## Slide 5: Floating Point Representation (example)
Thus the exponent is given by:
1 10000001 10101000000000000000000
From: Patt and Patel, pp. 34
S
biasedexponent
fraction
23
8
1
P-H. Section 3.5

## Slide 6: Floating Point Representation (example)
0011 1101 1000 0000 0000 0000 0000 0000
What is the decimal value of the following floating point number?
biasedexponent
biasedexponent = 27 – 23 + 3 = 128 - 8 + 3 = 123
From: Patt and Patel, pp. 34
S
biasedexponent
fraction
23
8
1
P-H. Section 3.5

## Slide 7: Answering Dylan Ashley's Question (Fall 2014)
Why the IEEE standard uses the bias format for the exponent
instead of a two-complement representation? Why?

## Slide 9: How to find the answer?

## Slide 11
1. Download the .pdf
2. Use search into the .pdf for what you want to find.
Example: "bias"

## Slide 13: Example
Problem: Compare 2.5 and 0.25. Which is larger?
2.5 = 21 + 2-1 = 10.1 × 20 = 1.01 × 21
0.25 = 2-2 = 0.01 × 20 = 1.0 × 2-2

## Slide 14: Example
Problem: Compare 2.5 and 0.25. Which is larger?
Representation with exponent in two complement:
Representation with exponent in bias representation:
2.5 = 1.01 × 21
0.25 = 1.0 × 2-2
2.5 = 0 10000000 01000000000000000000000
0.25 = 0 11111110 00000000000000000000000
-2 = 11111110
2.5 = 0 00000001 01000000000000000000000
0.25 = 0 01111101 00000000000000000000000

## Slide 15: Example
Problem: Compare 2.5 and 0.25. Which is larger?
Representation with exponent in two complement:
Representation with exponent in bias representation:
2.5 = 1.01 × 21
0.25 = 1.0 × 2-2
2.5 = 0 10000000 01000000000000000000000
0.25 = 0 11111110 00000000000000000000000
2.5 = 0 00000001 01000000000000000000000
0.25 = 0 01111101 00000000000000000000000
Using integer comparison:
2.5 < 0.25
Using integer comparison:
0.25 < 2.5

## Slide 16: Floating Point Representation (example)
0100 0001 1001 0100 0000 0000 0000 0000
What is the decimal value of the following floating point number?
biasedexponent =128+2+1=131
From: Patt and Patel, pp. 35
biasedexponent
S
biasedexponent
fraction
23
8
1
P-H. Section 3.5

## Slide 17: Floating Point Representation (example)
Thus the exponent is given by:
1 10000001 10101000000000000000000
From: Patt and Patel, pp. 34
S
biasedexponent
fraction
23
8
1
P-H. Section 3.5

## Slide 18: Floating Point
What is the largest number that can be represented in 32 bits floating
point using the IEEE 754 format above?
01111111011111111111111111111111
biasedexponent
biasedexponent =254
From: Patt and Patel, pp. 35
S
biasedexponent
fraction
23
8
1
P-H. Section 3.5

## Slide 19: Floating Point
What is the largest number that can be represented in 32 bits floating
point using the IEEE 754 format above?
actual exponent =254-127 = 127
From: Patt and Patel, pp. 35
S
biasedexponent
fraction
23
8
1
01111111011111111111111111111111
biasedexponent
P-H. Section 3.5

## Slide 20: Floating Point
What is the smallest number (closest to zero) that can be represented
in 32 bits floating point using the IEEE 754 format above?
00000000000000000000000000000001
actual exponent =0-126 = -126
From: Patt and Patel, pp. 35
S
biasedexponent
fraction
23
8
1
biasedexponent
P-H. Section 3.5

## Slide 21: Special Floating Point Representations
In the 8-bit field of the exponent we can represent numbers from 0 to
255. We studied how to read numbers with exponents from 0 to 254.
What is the value represented when the exponent is 255 (i.e. 111111112)?
An exponent equal 255 = 111111112 in a floating-point representation
indicates a special value.
When the exponent is equal 255 = 111111112 and the fraction is 0,
the value represented is ± infinity.
When the exponent is equal 255 = 111111112 and the fraction is
non-zero, the value represented is Not a Number (NaN).
P-H. Section 3.5

## Slide 22: A Possible Final Exam Question
Write a subroutine called fptoint that receives a 32-bit floating
point number f in IEEE 754 format and returns i, the integer portion
of the number expressed in two-complement.
Assume that the integer portion of the number is small enough
to be represented in a two-complement 32-bit representation.
S
biasedexponent
fraction
23
8
1

## Slide 23
t1 ← f >> 23
t2 ← t1 & 0x00ff # t2←bexponent
t3 ← 0x007f ffff
t4 ← f & t3 # t4←fraction
t5 ← 0x0080 0000 # bit 23 is 1
# add the 1 of 1.fraction
t4 ← t4 | t5
S
biasedexponent
fraction
23
8
1
if(t2 <= 126)
return 0
t6 ← t2-127 # exponent -127
t7 ← 23 – t6 # how much to move binary point
if t7 >= 0
i ← t4 >> t7
else
i = t4 << (-t7)
if(f<0)
i = - i
return i
srlv rd, rt, rs
S
bexponent
t1
bexponent
t2
fraction
t4
1
* with thanks to
Stephen Rebstock
and
Douglas Schneider